## Slide 1
A Versatile Multi-Robot Monte Carlo Tree Search Planner for On-Line Coverage Path Planning
Phillip Hyatt Zachary Brock Marc D. Killpack
Presentation prepared by
Yusuf Kursat Tuncel, Engin Tureli
201971003 | 201971007
Cankaya University, 2020, CENG 621 Course

## Slide 2
Introduction
This paper compares two search algorithms that are used in multiple coordinated intelligent agents such as vacuuming, seeding, harvesting, painting, search and rescue, and inspection.
This process is known as Coverage Path Planning (CPP)
Classical search algorithm: Boustrophedon search
The one examined in this research: Monte Carlo Tree Search (MCTS) for multiple robots in coordination.
The paper does not insist that MCTS is the best algorithm but it’s the most versatile (ability to adopt changes)

## Slide 3
All experiments were carried out in a real-time simulation
on an Intel i7-4770 processor using C++ and the Robot Operating System (ROS).
At least 50 times same simulation is run, average values are takes
Assumed no communication failures occurs
Assumed no sensors failed
Simulations

## Slide 4
Simulations

## Slide 5
Boustrophedon search
Meaning: Ox-turning in Greek

## Slide 6
Single Agent Boustrophedon search

## Slide 7
Monte Carlo Tree Search (MCTS)
Mainly used in game design, based on A* search
Adds repeated random sampling known as Monte Carlo Simulation (Monte Carlo is a famous casino in Monaco)
4-Steps
  Selection
  Expansion
  Simulation
  Backpropagation
Popular with Alpha-Go implementation, 2007

## Slide 8
Multi-Robot Coverage Path Planning
Does not depend on cellular composition
Can be used online for unknown areas
Each robot builds its own search tree, which makes the parallelization of the algorithm easier
Share only discovered map, the best path, covered grid squares
Before an action, they bid for the lowest cost and take action accordingly
Default policy: Move straight until ahead square is either occupied or already covered.

## Slide 10
Results
Varying number of robots
For robots 3 or more, MCTS performs slightly better than Boustrophedon.
Varying obstacle density
Very slighly increases, if at all, completion time of both algorithms.
No significance change in comparison.
Varying objectives
MCTS requires no change in the algorithm, only objective function is changed.
Boustrophedon requires addition of other algorithms for coordination.
MCTS performs comparable with “no cost on turning” objectives.
(no left turn, no right turn, no cost on turning)